## Slide 1
Basic Information
On Tender for
Resurfacing of runway 15-33, reconstruction of Taxiway A and other improvement works at Paro International Airport, Bhutan. (Civil Works)

## Slide 2: Brief Scope of Work
Re-surfacing of runway (Length 2270m, Width 30m, shoulder 5m on either side)
Taxiway-A – To be reconstructed with flexible pavement
Apron (30% slabs to be re-surfaced with cement slurry, 7% joints to be cut and fill and remaining joints to be cleaned and replace with joint seal)
Taxiway-B - Joints to be repaired

## Slide 3: Contd..
Both runway end turn pad joints to be repaired. Turn pad at RWY 33 shoulder to be reconstructed.
Marking to be done for runway, taxiways and apron.
Runway & Taxiway strip to be leveled.
RESA to be Constructed.
Drains to be cleaned and repaired

## Slide 4: Mandatory (Minimum) Construction Equipment
S. No. | Equipment Description | Capacity
01. | Computerized Bitumen Hot Weigh Batch mix plant | 1 No. 100 Ton / Hour OR 2 nos 60 ton/hour
02. | Computerized concrete Weigh Batch mix plant | 30 Ton / Hour
03. | Electronic Operated Sensor paver | 1 Nos. Adequate Width (extendable up to minimum 7.5m)
04. | Mechanical Paver | 1 No.
05. | Vibratory Roller (8 – 10 T) | Minimum 2 Nos.
06. | Pneumatic Roller (12-15T with tier Pressure of at least 0.56mpa .) | Minimum 2 No.
07. | Tippers / Dumpers 16cu.m capacity | Minimum10 Nos.

## Slide 5: Contd..
S. No. | Equipment Description | Capacity
08. | Truck mounted Mechanical Bitumen sprayer | 2 nos.
09. | Tractor mounted sweeper | 2 no.
10. | Air-compressor | 2 no.
11. | Concrete Joint cutting machine | 1 no.
12. | Front end Loader of bucket capacity of approx. 1 cum | 2 no.
13. | JCB | 1 no.
14. | Motor Grader | 1 no.
15 | Concrete Bracker | 1 no.
16 | Water taker | 1 no.

## Slide 6
S. No. | Equipment Description | Capacity
17 | Dozer | 1 no.
18 | Milling machine | 1no

## Slide 7: List of Engineers Required
Designation | Qualification | Nos. | Experience
Project Engineer | BE/B.Tech Civil | 1 | Min. 10 years in Bituminous Works in Airports
Civil Engineer | BE/B.Tech | 2 | Min. 5 years experience in Bituminous Works in Airport/ National Highways
Material Engineer | Minimum Diploma | 1 | Min. 5 years experience in Bituminous Works in Airport/ National Highways
Surveyor |  | 1 | Min. 5 years experience in Total Station, Digital Levelling.

## Slide 8: Equipment for Night working
Contractor shall execute the work during the night and Nothing extra shall be payable to contractor for working in night time.

## Slide 9: Contd..
For proper execution, the work site shall be properly illuminated and the following arrangement shall be made by the contractor at his own expenses :-
Two Nos. of DG sets of 25 KVA capacity of each with mobile arrangement to give illumination of 16 nos. of 1000 watt halogen lamps with suitable wiring shall be installed at the work site.
Pumps with Gensets to bail out water/mud encountered during excavation of earth i.e. dewatering wherever required..
No Construction equipment shall be supplied by the DoAT.

## Slide 10: Laboratory Equipment Required
1. | Apparatus For Aggregates And Soil | Nos.
i) | Aggregate Impact Value Test apparatus | 1 Set
ii) | Flakiness and Elongation Test Gauges. | 1 Set
iii) | Standard measure of 30, 15 and 3 liters capacity along with standard tamping rod. | 2 Set.
iv) | Mold for cube test | 12 Nos.
v) | Slump Cone | 1 Nos.
vi) | Atterberg Limits (liquid and plastic limits) determination apparatus. | 1 Set
vii) | Compaction Test Equipment both 2.5 kg and 4.5kg rammers (Light and Heavy compactive effort). | 1 Set
viii) | Dry Bulk Density Test apparatus (sand pouring cylinder, tray, can etc.) complete. | 1 Set
ix) | Speedy Moisture Meter Complete with chemicals | 1 Set
x) | Core cutter apparatus 10cm dia, 10/15 cm height, complete with dolly, rammer etc. | 1 Set

## Slide 11: Contd..
2. | Apparatus for testing of Bituminous Concrete | Nos.
i) | Marshall testing equipment | 1
ii | Water bath | 1
iii | Binder Extraction equipment | 1
iv | Bitumen Core cutting equipment | 

## Slide 12: Contd..
C. | GENERAL | 
i) | Balance 20 kg capacity-self indicating type | 1 No.
ii) | Electronic Balance 5 Kg capacity 0.5 gm. | 2 Nos.
iii) | Thermometers: Mercury-in glass thermometer range 0 to 250 deg C. Mercury-in steel thermometer with 30 cm stem, range upto 300 deg C. | 2Nos.
iv) | Electric Oven/ electric hot plate/ Kerosene or gas stove. | 1 No.
v) | Set of IS sieves with lid and pan with mechanical shaking arrangement; 450 mm diameter : 65mm, 40mm, 25mm, 12.5mm, 10mm and 4.75mm size and any other sieve required at site. | 2 Sets.
vi) | 200 mm diameter : 2.36mm, 2.0mm, 1.18mm, 600 micron, 425 micron, 300 micron, 150 micron and 75 micron and any other sieve required at site. | 2 Sets.
vii) | Water Testing Kit | 1 Set
viii) | First Aid Box | 1 Set

## Slide 13: Important Instruction to Bidder
Contractor shall establish his own lab with new equipment at DoAT’s premises. Space will be provided by DoAT.
Construction timing will be 1pm to 5am.
The project shall not hamper the daily airport operations
Hot batch mix plant to be established at the client premises, area will be provided by DoAT.
Construction Material like aggregate, fines, bitumen shall be stored at least for 7 days.
Safety precaution to be taken for labour, engineers.
Note: This presentation is a basic information of the project. The final and detailed project requirements and evaluation criteria shall be as per the bidding document which shall be uploaded on our website www.doat.gov.bt on 22nd Jan 2020.